## Slide 1: I/O Principles of I/O Hardware

## Slide 2: Review
File System
  Manages the information stored and hides the complexity on the storage devices
  Provides the users access information in a convenient way and a uniform logical view
  Is stored on disks
  Implementations
    File: Contiguous, Linked List, Linked List using a Table in Memory (FAT), i-nodes (same as multi-level paging)
    Directory: Fixed size entries, one per file containing file name & attributes
    File Name: fixed size, part of block, stored in heap
    Utilities:
      LFS (write data to end the log and using cleaner thread)
      JFS (store log file and using atomic transaction)
      VFS (uniform logical view for file system)
      Disk Space management
        Manage free block – linked list and bitmap
        Disk quota: two tables contain open file and user quotas

## Slide 3: Review
File System
  Implementations
    Utilities:
      Disk Space management
        File consistency: two array, one for block in use, other for free block
        Directory consistency: counter file and traversal i-node
        Backups, performance – caching
        Block read ahead: load block k + 1 to memory when the block k is accessed
        Reduce disk arm motion, defragmentation
File
  Abstraction, Object and Mechanism
  Name, Path (absolute vs. relative), Structure, Type, Access, Attributes, Operations
  Directory (Single level vs. Hierarchy)
  Sharing
    Traditional /hard linking (using one i-node)
    Symbolic linking (using larger than one i-node that references to path of file)

## Slide 4: Objectives
Principles of I/O Hardware
  I/O Devices
  Device Controllers
  Memory-Mapped I/O
  Direct Memory Access (DMA)
  Interrupts Revisited

## Slide 5: Principles of I/O Hardware
There are 2 categories: block devices and character devices
Block devices
  Store information in fixed-size blocks, each one with its own address
  Common block sizes range from 512 bytes to 32.768 bytes
  All transfers are in units of one or more entire (consecutive) blocks
  The essential property of block device is that it is possible to read or write each block independently of all the others ones
  Hard disks, CD-ROMs, and USB sticks
Character devices
  Deliver or accept a stream of characters, without regard to any block structure
  Is not addressable and does not have any seek operation
  Printers, mice …
The model of block and character devices is general enough that they can be used as a basic for making some OS software dealing with I/O device independent
I/O devices cover a huge range in speeds, which puts considerable pressure on the software to perform well over orders of magnitude in data rates
I/O Devices

## Slide 6: Principles of I/O Hardware
Is an electronic component in I/O units
Often takes the form of a chip on the parent board or a printed circuit card that can be inserted into a expansion slot
The controller card usually has a connector where the cables can be plugged
Many controllers can handle 2,4,6 or 8 identical devices
If the interface between the controller and device is a standard interface (ANSI, IEEE, ISO), then companies can make controllers or devices that fit that interface (ex: IDE, SATA, SCSI, USB, IEEE 1934)
The interface between the controller and the device is often a very low level interface
The controller’s job to convert the serial bit stream into a block of bytes and perform any error correction necessary
Device Controllers

## Slide 7: Principles of I/O Hardware
Context
  Each controller has a few registers that
    Can communicate with the CPU.
    Allow to read and write
  Many devices have a data buffer allow to read and write
→How the CPU communicates with control registers & device data buffers?
First approach
  Each controller register is assigned an I/O port number, an 8/16 bit integer
  The set of all the I/O ports form the I/O port space and is protected
  CPU can read contents from PORT to store in REG and can write the contents from REG to PORT
  → address spaces for memory and I/O are different
Memory-Mapped I/O
Tanenbaum, Fig. 5-2.

## Slide 8: Principles of I/O Hardware
Second approach
  Map all the control registers into the memory space
  Each control register is assigned a particular and unique memory address (Usually, the assigned addresses are at the top of the address space)
  → memory-mapped I/O with one address space
Combination approach
  A hybrid schema, with memory-mapped I/O data buffers and separate I/O ports for the control registers
Memory-Mapped I/O
Tanenbaum, Fig. 5-2.

## Slide 9: Principles of I/O Hardware
How do they work?
  When the CPU wants to read a word, either from memory or from an I/O port, it puts the address it needs on bus address lines and then asserts a READ signal on a bus' control line
  A second signal line is used to tell whether I/O space or memory space is needed
  If it is memory space, the memory responds to the request
  If it is I/O space, the I/O device responds to the request.
  If there is only memory space, every memory module and every I/O device compares the address lines to range of addresses that it services
  If the address falls in its range, it responds to the request. Since no address is ever assigned to both memory and an I/O device, there is no ambiguity and no conflict
Memory-Mapped I/O
Notes: Ambiguity: mơ hồ, không rõ ràng

## Slide 10: Principles of I/O Hardware
Advantages
  A I/O device driver can be written entire in C (instead of using complexity assembly code)
  No special protection mechanism is needed to keep user processes from performing I/O
  Every instruction that can reference memory can also reference control registers (using one instruction instead of two)
Disadvantages
  Caching a device control register would be disastrous (reference from cache instead of devices → disable cache is a solution)
  The I/O devices have no way of seeing memory addresses as they go by on the memory bus, so they have no way of responding to them
  The need of figuring out at boot time which memory addresses are not really memory addresses
Memory-Mapped I/O
Notes: Disastrous: tai hại

## Slide 11: Principles of I/O Hardware
Problem
  Disk controller reads the block from the drive serially, bit by bit, until the entire block is in the controller’s internal buffer
  Disk controller computes the checksum to verify that no read errors have occurred
  Disk controller interrupts the CPU to let know that those tasks are completed
  CPU reads the disk block from the controller’s buffer a byte or a word at a time by executing a loop, with each iteration reading on byte or word from controller device register and storing it in main memory
  → waste the CPU’s time
Solution
  Using DMA
Direct Memory Access – DMA

## Slide 12: Principles of I/O Hardware
The DMA controller is integrated into each device
The DMA controller has access to the system bus independent of the CPU
The DMA controller regulates transfers to multiple devices, often concurrently
The acknowledgement is used for each DMA channel to determine the serviced device.
The DMA controller contains several registers
  A memory address register
  A byte count register
  One or more control registers: specify the I/O port to use, the direction of the transfer (read/write from/to I/O device), the transfer unit (byte/word at a time), and the number of bytes to transfer in one burst
Direct Memory Access – DMA
Notes: The information about the number of bytes which are to be transferred using DMA are contained in the Counter Registers, which is decremented by 1 for every byte in the DMA data transfer. When the Counter Register becomes 0, the last DMA data transfer results in activating the terminal count (TC) output by 8257.

## Slide 13: Principles of I/O Hardware
Step 1
  The CPU sets the DMA controller registers so DMA knows what to transfer where, and how many transfer
  The CPU commands the disk controller read data from disk to internal buffer, then verify the checksum
Step 2
  The DMA controller initiates the transfer by issuing a read request over the bus to the disk controller
Step 3
  The disk controller transfer a word/ byte from internal buffers to main memory at the address that is described in the DMA’s memory address register
Step 4
  The disk controller sends an acknowledgement signal to DMA controller when the write is complete
  Simultaneously, the DMA controller decides which device to service next (using RR or priority scheme)
  In each transfer, the DMA controller increments the memory addresses to use and decrements the byte count
  If the byte count is still greater than 0, step 2 through 4 are repeated until the count reaches 0
  If the byte equals 0, the DMA controller interrupts the CPU to let it know the transfer is now complete
Direct Memory Access – DMA – Mechanism

## Slide 14: Principles of I/O Hardware
Direct Memory Access – DMA
Tanenbaum, Fig. 5-4.

## Slide 15: Principles of I/O Hardware
DMA can operate in three mode
  Word-at-a-time mode
    The DMA controller requests for the transfer of and gets one word
    Cycle stealing: CPU has to wait the bus because device controller sneaks in and steals an occasional bus cycle from CPU
  Block mode
    Burst mode: DMA tells the device to acquire the bus, issue a series of transfer, then release the bus (efficiently because transfer multiple words)
    Disadvantages: It can be blocked the CPU and other devices with long burst is being transfer
  Fly-by mode
    DMA tells the device controller to transfer the data directly to main memory
    To have the device controller send the word to the DMA controller, an extra bus cycle is provided per word transfer
    → Flexible in performing device to device copies and even memory-to-memory copies (first, read to memory, then write to a memory at a different address)
Direct Memory Access – DMA
Notes: Sneak: đánh lén

## Slide 16: Principles of I/O Hardware Direct Memory Access – DMA
DMA uses physical memory addresses
  OS convert the virtual address of the intended memory buffer into a physical address and write this physical address into the DMA controller’s address register
  Or, virtual addresses are written into the DMA controller, then DMA must use MMU to have the virtual-to-physical translation
Why does the controller need an internal buffer?
  The disk controller can verify the checksum before starting a transfer (Ensuring that the errors do not occur before transferring)
  Reduce the administration data in transfer when the bus were busy (then using DMA transfer because the DMA is not time critical)
Is the DMA faster or the CPU faster?
  The CPU is faster and can do the job much faster when the limiting factor is not the speed of the I/O device
Notes: Intended: chủ tâm

## Slide 17: Principles of I/O Hardware
Interrupts Revisited
Tanenbaum, Fig. 5-5.

## Slide 18: Principles of I/O Hardware
Leave the machine in a well-defined state
There are 4 properties
  PC is saved in a known place.
  All instructions before the one pointed to by the PC have fully executed.
  No instruction beyond the one pointed to by the PC has been executed.
  Execution state of the instruction pointed to by the PC is known
There is no prohibition on instructions beyond the one pointed to by the PC from starting.
Any changes make to registers or memory must be undone before the interrupt happens
→ chip is complexity in design
Precise Interrupts
Tanenbaum, Fig. 5-6.
Notes: A trap is an exception in a user process. It's caused by division by zero or invalid memory access. It's also the usual way to invoke a kernel routine (a system call) because those run with a higher priority than user code. Handling is synchronous (so the user code is suspended and continues afterwards). In a sense they are "active" - most of the time, the code expects the trap to happen and relies on this fact.
An interrupt is something generated by the hardware (devices like the hard disk, graphics card, I/O ports, etc). These are asynchronous (i.e. they don't happen at predictable places in the user code) or "passive" since the interrupt handler has to wait for them to happen eventually.
You can also see a trap as a kind of CPU-internal interrupt since the handler for trap handler looks like an interrupt handler (registers and stack pointers are saved, there is a context switch, execution can resume in some cases where it left off).
Prohibition: cấm

## Slide 19: Principles of I/O Hardware
Does not meet all requirements as precise
Different instructions near PC are in different stages of completions
Machines with imprecise usually vomit a large amount of internal state onto the stack to give the OS the possibility of figuring out what was going on.
  →The code necessary to restart the machine is typically extremely complicated
  →Saving a large mount of information to memory on very interrupts make interrupts slow and recovery even worse
Imprecise Interrupts
Tanenbaum, Fig. 5-6.
Notes: In computing, a pipeline, also known as a data pipeline,[1] is a set of data processing elements connected in series, where the output of one element is the input of the next one. The elements of a pipeline are often executed in parallel or in time-sliced fashion. Some amount of buffer storage is often inserted between elements.

## Slide 20: Summary
Principles of I/O Hardware
Q&A

## Slide 21: Next Lecture
Principles of I/O Software
I/O Software Layers